Project Name:

SECTION 12492

Manual Solar Shades

# Part 1 - General

# DESCRIPTION

- Manual solar shades

  - SUBMITTALS

- Manufacturer’s complete CSI 3- part specification sheet.

- Submit working hand sample or mock up shade as required.

- Submit two 4” x 6” samples of shade fabric material indicating color and dimensions.

  - DELIVERY, STORAGE AND HANDLING

- Product to be delivered in manufacturer’s original packaging.

- Products to be handled and stored to prevent damage to materials, finishes and operating mechanisms. Store in a clean, dry area, laid flat to prevent sagging and twisting of packaging.

  - EXTRA STOCK

- Describe extra attic stock as required:

# PART II - PRODUCTS

  - Manufacture and Product Description

- EcoGreen Solar Shades, LLC.
Phone: 877-610-1555
Email: Sales@EcoGreenSolarShades.com

- Substitution Request: Submit for approval under provisions of section

  - Manual Solar Shades

- Product: EGSS contract manual solar shade

- Solar shade fabric shall be flame retardant, fade and stain resistant, anti-static, anti-microbial and pass NFPA 701-1999 FR and ASTM-G21 and G22.  Shades with railroaded fabric will have heat-welded seams. Fabric shall be selected by architect from SWFcontract fabric collection.

Fabric Style:      Color Name:      Color Number:

  - Roller tube shall be extruded aluminum engineered with a channel to accept fabric spline. The tube size will be determined by the manufacturer based on window size and fabric selection.

  - Clutch system shall be made of glass-reinforced, polyester thermopolymer (PBT) for wear resistance, smooth operation and corrosion resistance.  The clutch is comprised of multi-banded, steel springs that lock the shade in any  position when operating the control loop. The clutch mechanism is bi-directional and never requires adjustment or lubrication.

  - Control loop shall be a #10 stainless steel bead chain.  Bead stops attached to the chain protect the shade from over rotation. Optional plastic bead chain is available in vanilla and black.

  - Idler end shall be made of high strength, glass-reinforced, polyester thermopolymer (PBT) for wear resistance, smooth operation and corrosion resistance.

  - Lift assist system shall be a heavy-duty torsion spring located inside the roller tube. The mechanism reduces the pull force allowing easy lifting of larger shades.

  - Spline system shall consist of a PVC spline heat-welded to the shade fabric and inserted into a channel on the roller tube.  The spline system allows for adjustability on-site and ease in changing fabric panels in the field.

  - Hem bar shall be an aluminum extrusion enclosed in a fabric hem pocket with heat-welded seams and ends. Optional fabric wrapped hem bar.

  - Battens shall be enclosed in a heat-welded pocket providing additional stabilizing on large shades. Batten placement will be determined by the manufacturer based on window size and fabric selection.

  - Installation brackets shall be .125” thick steel and can accommodate overhead, side and face mounting. Optional dual shade brackets shall hold two shades in one bracket assembly. Coupled shades shall be connected with a linking bracket mechanism.

  - OPTIONAL ACCESSORIES

Fascia panel shall be 3 ” (low voltage systems only), 4.25" or 7.625” dual shade snap-on design and made of 062” thick extruded 6063 T-5 aluminum alloy with a powder-coated finish.  Brackets shall be universal and painted to match the fascia panels.

Select color:     white  vanilla  clear anodized  bronze  black

Shade pocket shall be 4.75” x 5” powder-coated extruded 6065-aluminum alloy or 7.5” x 8” white powder-coated steel.  SWF shall provide appropriate dimensional pocket as necessary to enclose roller tube and fabric.

Select color:   white  clear anodized  bronze anodized

Closure plate shall be exposed, flush mounted, powder-coated extruded 6065-aluminum alloy designed to provide access to shades when recessed in ceiling. Plates are available in 2”, 3” or 5” with or without a tile support for acoustical tiles.

Select color:   white  clear anodized  bronze anodized

Side, sill and/or center channels shall be a two-piece design made of powder-coated extruded 6065-aluminum measuring 2” x 1” and includes synthetic pile inserts to eliminate light leakage.  A 4” x 1 center channel is provided for coupled blackout shades.

Select color:   white  clear anodized  bronze anodized

2.04 FABRICATION

- Shades shall be fabricated according to specifications and accurate to tolerance established by SWF engineering standards.

- Fabricate shades to hang flat without buckling or distortion.

PART 3 – EXECUTION

3.01 INSPECTION

- Installer shall be responsible for inspection of jobsite, approval of mounting surfaces, blocking for shade brackets or pocket assemblies, suspended acoustical or gypsum ceiling for recessed shades, verification of field measurements and installation conditions. Installation shall commence when satisfactory conditions are met.

3.02 INSTALLATION

- Install shades in accordance with manufacturer’s instructions including recommended support brackets and fasteners.

- Install shades with adequate clearance to permit smooth operation of the shades throughout entire operational range. Installer will demonstrate shades to be in smooth, uniform working order.

- Architectural and electrical drawings may or may not indicate the motor or motor controller wiring.  All motors and controllers must be wired according to specifications and wiring diagrams prior to installation of motorized shades, as provided by installer/dealer, according to manufacturer’s product requirements.

3.03 MAINTENANCE AND CLEANING

- Shades may be vacuumed with a soft brush attachment or cleaned with mild soap and water solution. Do not use cleaning methods involving heat, bleach, abrasives, or solvents. Use of these methods will void the warranty.

# END OF SECTION